## Slide 1
CHALMERS UNIVERSITY OF TECHNOLOGY | MMS236 AIRCRAFT DESIGN | DESIGN TASK 1
EXAELIA
80m Long-Range Liquid Hydrogen Blended Wing Body Transport
Group 13 Design Team:
Johan Persson • Sai Srinivasa Manideep Jakka • Tobias Hilltorp • William Gustavsson
PASSENGER CAPACITY
430 Pax (2-Class)
DESIGN RANGE
12,500 km (6,750 nm)
CRUISE SPEED
Mach 0.85 at FL350
WINGSPAN
80.0 m (ICAO Code F)

## Slide 2
MMS236 AIRCRAFT DESIGN | GROUP 13
Concept Origin: From Initial Sketch to Blended Body Architecture
1. Pure 80m Wingspan (ICAO Code F Gate Box)
Full span compliant with existing international airport gates (A380/B777X class) without requiring folding wings.
2. Muscular Lifting Centerbody (t/c = 19.5%)
A 7.41 m maximum centerbody depth easily houses a stand-up widebody passenger cabin and multi-layer cryogenic tanks.
3. Unified Single-Deck Theater Cabin (430 Pax)
Continuous 14.0 m wide central passenger deck with uninterrupted longitudinal aisles, eliminating claustrophobic isolated rows.
4. Symmetrical Outboard & Aft Cryotanks (610 m³)
6 double-walled vacuum-insulated cylinders placed in wing shoulders and aft core to minimize CG excursion during fuel burn.
5. Upper-Deck Acoustically Shielded Turbofans
Twin geared turbofans mounted above the trailing deck to shield airport communities from engine fan and jet noise.

## Slide 3
MMS236 AIRCRAFT DESIGN | GROUP 13
Mission Profile & Flight Operational Envelope
MAIN CRUISE SEGMENT
12,500 km at FL350 (M0.85)
ALTERNATE AIRPORT DIVERSION
200 nm at FL250 (CS-25)
STATUTORY LOITER & CONTINGENCY
30 min + 3% at 1,500 ft (ICAO)

## Slide 4
MMS236 AIRCRAFT DESIGN | GROUP 13
Propulsion Modeling: Liquid Hydrogen SFC & Energy Density
Year 2050 EIS Turbofan Baseline (Jet-A):
Following historical efficiency trends (CFM56 ➔ GE90 ➔ Leap-1A): • Jet-A Cruise SFC: ~12.0 to 13.5 mg/(N·s) • Jet-A Loiter SFC: ~11.0 mg/(N·s)
Thermal Energy Equivalence Principle:
Hydrogen releases 2.80× higher energy per kg than kerosene: • LHV (Jet-A) = 42.8 MJ/kg • LHV (LH2) = 120.0 MJ/kg • Energy Ratio: 42.8 / 120.0 = 0.3567
Converted Liquid Hydrogen SFC:
• LH2 Cruise SFC = 12.0 × 0.3567 ≈ 4.80 to 4.815 mg/(N·s) • LH2 Loiter SFC = 11.0 × 0.3567 ≈ 3.92 mg/(N·s) ➔ Over 60% lower fuel mass flow rate than conventional Jet-A!

## Slide 5
MMS236 AIRCRAFT DESIGN | GROUP 13
Aerodynamic Efficiency & Drag Polar Optimization
ASPECT RATIO (AR)
9.50 Transonic Optimum
WETTED RATIO (SWET/SREF)
2.20 High Volume Hull
MAX EFFICIENCY (L/D MAX)
30.8 Loiter & Hold Phase
CRUISE EFFICIENCY (L/D)
26.7 Mach 0.85 Range Max
Parabolic Drag Polar Formulation:
• Zero-Lift Drag (CD0): 0.0150 (smooth composite BWB surface) • Oswald Span Factor (e): 0.85 with 70° canted winglets • Optimal Lift-to-Drag Ratio: (L/D)_max = 0.5 × sqrt(π × AR × e / CD0) • Long-Range Cruise Condition: (L/D)_cruise = 0.866 × (L/D)_max (maximizes V × L/D range factor)
Blended Wing Body Advantages:
• Lifting Fuselage: Centerbody generates ~45% of total aircraft lift, reducing required wing loading. • Lower Wetted Area per Passenger: Reduces parasitic drag per seat by ~20% compared to circular tube-and-wing. • Spanwise Camber & Winglets: Endplates lower induced drag while remaining strictly within the 80m Code F gate limit.

## Slide 6
MMS236 AIRCRAFT DESIGN | GROUP 13
Aircraft Weight Buildup & Sizing Convergence
Mass Breakdown (Converged Sizing Model):
• Maximum Take-Off Weight (MTOW) : 235,460 kg (235.5 t) (100.0%)
• Operating Empty Weight (OEW / We) : 155,600 kg (155.6 t) (66.0%)
• • Baseline Airframe & Systems : 120,200 kg (120.2 t) (51.0%)
• • Cryogenic LH2 Tanks (6 Tanks) : 35,400 kg (35.4 t) (15.0%)
• Design Payload (430 Pax + Cargo) : 53,750 kg (53.8 t) (22.8%)
• Usable Liquid Hydrogen Fuel : 24,850 to 39,330 kg (~11–17%)
• Flight & Cabin Crew (12 Crew) : 1,260 kg (1.26 t) (0.5%)
Cryotank Gravimetric Sizing:
• Gravimetric Index (Gi = 0.50): Gi = M_fuel / (M_fuel + M_tank) Dry tank structural mass equals fuel mass. • 6 Cylindrical Vessels: 4 Wing Shoulder + 2 Aft Core tanks. Average Dry Mass = 5,900 kg / tank. • Thermal & Pressure Boundary: - 20.3 K (-253 °C) liquid temperature - 2.0 bar operating pressure - Double-walled Multi-Layer Insulation (MLI) with evacuated vacuum jacket.

## Slide 7
MMS236 AIRCRAFT DESIGN | GROUP 13
The Concept: 80m Blended Wing Body Digital Blueprint

## Slide 8
MMS236 AIRCRAFT DESIGN | GROUP 13
3D Parametric CAD Model & Surface Mesh (OpenVSP 3.51.3)

## Slide 9
MMS236 AIRCRAFT DESIGN | GROUP 13
Design Innovations & Future Work (Design Task 2)
1. Unified Passenger Deck
• 430 Pax widebody theater layout (20m × 14m × 2.4m). • 4 continuous aisles with rapid emergency evacuation egress. • Eliminates isolated rows while preserving generous stand-up headroom.
2. Balanced Fuel Packaging
• 6 symmetrical cryotanks placed in wing shoulders and aft core. • Minimal CG travel during flight, avoiding trim drag penalties. • Total storage volume: 610 m³ liquid hydrogen.
3. Acoustic Shielding & Ops
• Twin top-mounted turbofans shielded by upper aft deck. • 80m span strictly respects ICAO Code F airport infrastructure. • 3-point heavy landing gear ensures ground clearance.
Roadmap for Design Task 2 (DT2 Detailed Aerodynamics & Structure):
• 3D High-Fidelity CFD in Siemens STAR-CCM+ to validate transonic cruise polars (M0.85, Re = 45M). • Finite Element Structural Optimization for multi-bubble pressurized cabin bulkheads and wing spars. • Dynamic Stability & Control evaluation with winglet rudders and elevon sizing.

## Slide 10
MMS236 AIRCRAFT DESIGN | GROUP 13
Academic & Industry References
NASA Technical Reports Server (NTRS)
NASA/CR-2012-217578: Aerodynamic Design and Performance Analysis of Advanced Blended-Wing-Body Transports
Source: https://ntrs.nasa.gov/api/citations/20120001452/downloads/20120001452.pdf
International Journal of Hydrogen Energy (ScienceDirect)
Cryogenic Hydrogen Fuel Storage, Boil-off Management, and Sizing for Long-Range Civil Transports (2024)
Source: https://www.sciencedirect.com/science/article/pii/S036031992404535X#bib87
Aircraft Design: A Conceptual Approach (D.P. Raymer, 6th Ed.)
Statistical empty weight estimation, Breguet jet range sizing algorithms, and CS-25 reserve fuel compliance.
Source: AIAA Education Series (2018)
Chalmers University of Technology MMS236 Lecture Series
Lecture 2 (Atmospheric Modeling & Sizing Loops), Lecture 4 (Propulsion Trends & Cryogenic Hydrogen Aviation).
Source: Department of Mechanics and Maritime Sciences (2026)